## Slide 1: Quality Control Circle: Endless Innovation
Project Title:
Rectification of primary dust catcher (PDC) cooling pipes
JSW Steel Ltd, Dolvi
https://1drv.ms/p/c/096c43f5cc6632e3/EQJzfiv8jA5BhPR8O015DmABzDLOliAucV1AK9GIJMLf0A

## Slide 2
The flagship company of JSW Group, JSW Steel is one of India’s leading integrated
steel manufacturers with a capacity of 18 million tons per annum(MTPA).
By 2025, JSW Steel aims to produce 40 MTPA.
JSW Steel Ltd, Dolvi

## Slide 3
JSW Steel Ltd, Dolvi

## Slide 4
JSW Steel Ltd, Dolvi
Quality Circle Team Charter
TIC | Coke Oven & Refractory | HOD | Mr. Sanjay V. Gurme
Department | Coke Oven II | Day & Time of meeting | Every Saturday
Section/ Area | CDQ2&3 | No. of Problems Identified | 37
Date of Formation |  | Problems Solved | 1
Registration No: | QCPR/FY2023-2024/QCC/Coke Oven & Refractory/Coke Oven-2/58/838 | Team Details: | 
 |  | Leader | Mr. Sagar Kumar Singh
Name of QC Circle | ENDLESS INNOVATION | Member 1 | Mr. Sumant kumar
 |  | Member 2 | Mr. Bishwajeet Singh
 |  | Member 3 | Mr. Mukul Kumar
Facilitator | Mr. Shreyan Koshti | Member 4 | Mr.Sonu Ansari
Process Owner | Mr. D.B. Varaprasad |  | 

## Slide 5
JSW Steel Ltd, Dolvi
STEP - 1
IDENTIFICATION OF PROBLEMS
Technique used : Brain Storming

## Slide 6
JSW Steel Ltd, Dolvi
Sl. No. | PROBLEM | Sl. No. | PROBLEM | Sl. No. | PROBLEM
1 | RSV Trip for Liner | 16 | Loco Bucket indication problem | 31 | Gas Circulation Fan Drive issue
2 | Nitrogen Consumption High than Design | 17 | APS Indication problem | 32 | ID fan drive issue
3 | GCF Tripping for Low IA | 18 | Crane operation frequent stoppage for APS Signal issue | 33 | Gas Analyzer problem
4 | GDS vibrator not working | 19 | RSV Dust generation from Vibrofeeder | 34 | Frequently steam line leakages and steam trap failure
5 | GDS hopper level sensor not working | 20 | Water seal pump failure | 35 | Bucket Rotation Problem.
6 | GCF Inlet Damper not working | 21 | Bucket Elevator tripping issue | 36 | water seal pot pump trip issue
7 | Chamber slide gate not working | 22 | PDC SDC RAV jamming | 37 | LOCO bucket present indication issue
8 | PDC SDC level sensor not working | 23 | PDC Cooling pipe leakage |  | 
9 | Charging Hopper Alignment issue in Chamber | 24 | Radar sensor Malfunctioning |  | 
10 | Frequent conveyor stop resulting loss of Production | 25 | GDS Bag filter damaged |  | 
11 | Frequent Bucket Liner damage | 26 | GDS Discharge cylinder Issue |  | 
12 | Bucket Swapping takes time for unavailability of Carriage | 27 | Flow Chain conveyor trip issue for sensor failure |  | 
13 | Coke Conveyor Spillage | 28 | Seal pot jamming issue with Dust |  | 
14 | Frequent jamming of GDS Hopper | 29 | Visibility issue of Operator from Cabin |  | 
15 | Frequent jamming of Pugmill | 30 | Charging crane drive fault |  | 
Step 1 Identification of Problem
PROBLEM IDENTIFICATION BANK

## Slide 7
JSW Steel Ltd, Dolvi
STEP - 2
Selection of Problem
Tool used: Stratification and Bar graph

## Slide 8
JSW Steel Ltd, Dolvi
PROBLEM IDENTIFICATION BANK(A/B/C)
Step 2 Selection of Problem
Sl. No. | PROBLEM | PRIORITY |  |  | Sl. No. | PROBLEM | PRIORITY |  | 
1 | RSV Trip for Liner | A |  |  | 16 | Loco Bucket indication problem |  | B | 
2 | Nitrogen Consumption High than Design | A |  |  | 17 | APS Indication problem |  | B | 
3 | GCF Tripping for Low IA |  | B |  | 18 | Crane operation frequent stoppage for APS Signal issue |  | B | 
4 | GDS vibrator not working | A |  |  | 19 | RSV Dust generation from Vibrofeeder | A |  | 
5 | GDS hopper level sensor not working | A |  |  | 20 | Water seal pump failure | A |  | 
6 | GCF Inlet Damper not working | A |  |  | 21 | Bucket Elevator tripping issue | A |  | 
7 | Chamber slide gate not working |  |  | C | 22 | PDC SDC RAV jamming | A |  | 
8 | PDC SDC level sensor not working | A |  |  | 23 | PDC Cooling pipe leakage |  |  | C
9 | Charging Hopper Alignment issue in Chamber | A |  |  | 24 | Radar sensor Malfunctioning | A |  | 
10 | Frequent conveyor stop resulting loss of Production |  | B |  | 25 | GDS Bag filter damaged | A |  | 
11 | Frequent Bucket Liner damage |  | B |  | 26 | GDS Discharge cylinder Issue | A |  | 
12 | Bucket Swapping takes time for unavailability of Carriage |  |  | C | 27 | Flow Chain conveyor trip issue for sensor failure | A |  | 
13 | Coke Conveyor Spillage | A |  |  | 28 | Seal pot jamming issue with Dust | A |  | 
14 | Frequent jamming of GDS Hopper | A |  |  | 29 | Visibility issue of Operator from Cabin |  | B | 
15 | Frequent jamming of Pug mill | A |  |  | 30 | Charging crane drive fault | A |  | 
12
JSW Steel Ltd, Dolvi

## Slide 9
JSW Steel Ltd, Dolvi
PROBLEM IDENTIFICATION BANK(A/B/C)
Step 2 selection of Problem
Sl. No. | PROBLEM | PRIORITY |  | 
31 | Gas Circulation Fan Drive Fault | A |  | 
32 | ID fan drive Fault | A |  | 
33 | Gas Analyzer problem |  | B | 
34 | Frequently steam line leakages and steam trap failure |  | B | 
35 | Bucket Rotation Problem. | A |  | 
36 | water seal pot pump trip issue | A |  | 
37 | LOCO bucket present indication issue | A |  | 
13
Complexity:
A: Within Department
B: Cross Functional
C: Management Support

## Slide 10
JSW Steel Ltd, Dolvi
Chart: 
| A CATEGORY | B CATEGORY | C CATEGORY
No. of Problems | 25 | 9 | 3
Step 2 selection of Problem
Complexity | No. of Problems
A CATEGORY | 25
B CATEGORY | 9
C CATEGORY | 3
A- Within department
B- Cross functional
C- Management support
JSW Steel Ltd, Dolvi
BRAINSTROMING (A/B/C Analysis)

## Slide 11
JSW Steel Ltd, Dolvi
Sl. No. | LIST OF PROBLEM | Category A | QC /Kaizen | Sl. No. | LIST OF PROBLEM | Category A | QC /Kaizen
1 | RSV Trip for Liner | A | QC | 15 | Radar sensor Malfunctioning | A | QC
2 | Nitrogen Consumption High than Design | A | QC | 16 | GDS Bag filter damaged | A | Kaizen
3 | GDS vibrator not working | A | Kaizen | 17 | GDS Discharge cylinder Issue | A | QC
4 | GDS hopper level sensor not working | A | Kaizen | 18 | Flow Chain conveyor trip issue for sensor failure | A | Kaizen
5 | GCF Inlet Damper not working | A | Kaizen | 19 | Seal pot jamming issue with Dust | A | Kaizen
6 | PDC SDC level sensor not working | A | Kaizen | 20 | Charging crane drive fault | A | QC
7 | Charging Hopper Alignment issue in Chamber | A | Kaizen | 21 | Gas Circulation Fan Drive Fault | A | Kaizen
8 | Coke Conveyor Spillage | A | Kaizen | 22 | ID fan drive Fault | A | Kaizen
9 | Frequent jamming of GDS Hopper | A | Kaizen | 23 | Bucket Rotation Problem. | A | QC
10 | PDC Cooling pipe leakage | A | QC | 24 | water seal pot pump trip issue | A | Kaizen
11 | RSV Dust generation from Vibrofeeder | A | Kaizen | 25 | LOCO bucket present indication issue | A | Kaizen
12 | Water seal pump failure | A | Kaizen |  |  | A | 
13 | Bucket Elevator tripping issue | A | Kaizen |  |  | A | 
14 | PDC SDC RAV jamming | A | Kaizen |  |  | A | 
BRAINSTROMING (A/B/C Analysis)
Step 2 selection of Problem
JSW Steel Ltd, Dolvi

## Slide 12
JSW Steel Ltd, Dolvi
Sl.no. | LIST OF PROBLEM | Category A | QC /Kaizen | IMPACT |  |  |  |  |  | 
 |  |  |  | P | Q | C | D | M | E | S
1 | RSV Trip for Liner | A | QC | P | Q | C |  |  |  | S
2 | Nitrogen Consumption High than Design | A | QC |  | Q | C |  |  |  | 
10 | PDC Cooling pipe leakage | A | QC | P |  | C | D |  | E | S
15 | Radar sensor Malfunctioning | A | QC | P |  |  |  |  |  | S
17 | GDS discharge cylinder issue | A | QC |  | Q |  | D | M | E | 
20 | Charging crane drive fault | A | QC | P |  |  |  | M |  | 
23 | Bucket Rotation Problem. | A | QC |  |  |  |  |  |  | 
BRAINSTROMING (A/B/C Analysis)
Step 2 Selection of Problem
16

## Slide 13
JSW Steel Ltd, Dolvi
PROBLEM IMPACT ANALYSIS
Step 2 Selection of Problem
Impact | QCC
Productivity (P) | 4
Quality (Q) | 3
Cost (C) | 3
Delivery (D) | 2
Morale (M) | 2
Environment (E) | 1
Safety (S) | 3
2
Chart: QCC
| Impact | Productivity (P) | Quality (Q) | Cost (C) | Delivery (D) | Morale (M) | Environment (E) | Safety (S)
 | 4 | 3 | 3 | 2 | 2 | 1 | 3

## Slide 14
JSW Steel Ltd, Dolvi
LEVEL OF IMPACT
WEAK = 2 MEDIUM = 5 STRONG = 10
Sr. No. | Problem | Productivity | Quality | Cost | Delivery | Safety | Morale | Environment | Total
1 | RSV Trip due to liner |  |  |  |  |  |  |  | 28
2 | Nitrogen consumption is high than design |  |  |  |  |  |  |  | 28
3 | PDC Cooling pipe leakage |  |  |  |  |  |  |  | 42
4 | GDS Discharge cylinder Issue |  |  |  |  |  |  |  | 25
5 | Bucket Rotation Problem. |  |  |  |  |  |  |  | 23
THEME SELECTED :- Quality
BRAINSTROMING (A/B/C Analysis)
Selection of the Problem

## Slide 15
JSW Steel Ltd, Dolvi
PRIORITIZATION OF PROBLEMS(RATING METHOD)
Step 2 Selection of Problem
Sl. No. | List of Problems | FACILITATOR | LEADER | MEMBERS |  |  |  | 
 |  | Shreyan | Sagar | Sumant | Biswajeet | Mukul | Sonu | Total
01 | RSV trip for liner | 8 | 7 | 7 | 8 | 5 | 6 | 41
02 | Nitrogen consumption high than design | 8 | 7 | 6 | 7 | 6 | 5 | 39
03 | PDC Cooling pipe leakage | 9 | 8 | 8 | 9 | 8 | 8 | 50
03 | GDS discharge cylinder issue | 7 | 8 | 6 | 8 | 4 | 5 | 38
05 | Bucket rotation problem. | 8 | 6 | 6 | 6 | 5 | 6 | 37
LEAST | 0-3
MODERATE | 4-7
HIGH | 7-10
MARKS CRITERIA

## Slide 16
JSW Steel Ltd, Dolvi
Chart: 
| RSV Trip due to liner | Nitrogen consumption is high than design | PDC Cooling pipe leakage | GDS Discharge cylinder Issue | Bucket Rotation Problem.
 | 41 | 39 | 50 | 38 | 37
PRIORITIZATION OF PROBLEMS ANALYSIS
Step 2 Selection of Problem

## Slide 17
PROBLEM SELECTED
Step 2 Selection of Problem
JSW Steel Ltd, Dolvi
Primary dust catcher (PDC) cooling pipe leakage

## Slide 18
Sr. No | STEPS | P/A | Dec |  |  |  | Jan |  |  | 
 |  |  | W1 | W2 | W3 | W4 | W1 | W2 | W3 | W4
1 | Define the problem | Plan |  |  |  |  |  |  |  | 
 |  | Actual |  |  |  |  |  |  |  | 
2 | Analysis of problem | Plan |  |  |  |  |  |  |  | 
 |  | Actual |  |  |  |  |  |  |  | 
3 | Identification of causes | Plan |  |  |  |  |  |  |  | 
 |  | Actual |  |  |  |  |  |  |  | 
4 | Identification of root causes | Plan |  |  |  |  |  |  |  | 
 |  | Actual |  |  |  |  |  |  |  | 
5 | Data analysis | Plan |  |  |  |  |  |  |  | 
 |  | Actual |  |  |  |  |  |  |  | 
6 | Development of solution | Plan |  |  |  |  |  |  |  | 
 |  | Actual |  |  |  |  |  |  |  | 
7 | Foreseen resistance | Plan |  |  |  |  |  |  |  | 
 |  | Actual |  |  |  |  |  |  |  | 
8 | Trial Implementation | Plan |  |  |  |  |  |  |  | 
 |  | Actual |  |  |  |  |  |  |  | 
9 | Regular Implementation | Plan |  |  |  |  |  |  |  | 
 |  | Actual |  |  |  |  |  |  |  | 
10 | Follow up/Review | Plan |  |  |  |  |  |  |  | 
 |  | Actual |  |  |  |  |  |  |  | 
MILESTONE CHART

## Slide 19
JSW Steel Ltd, Dolvi
STEP - 3
DEFINE THE PROBLEMS
Tool used: Diagram

## Slide 20
COKE DRY QUENCHING-HIGH LEVEL DIAGRAM
JSW Steel Ltd, Dolvi

## Slide 21
PROBLEM STATEMENT- The problem lies in punctured PDC cooling pipes, which compromise the chain conveyor's health, lead to rust formation, and cause dust buildup in PDC hoppers. This, in turn, elevates boiler inlet pressure and exacerbates dust generation, deviating from design specifications. Rectifying or preventing these punctures is crucial for maintaining system efficiency and performance.
DEFINE THE PROBLEM
Step 3 Define the Problem
JSW Steel Ltd, Dolvi
Objective
Duration
Goal
Dust generation as per design,
Preventing PDC cooling pipe punctures which compromise the chain conveyor's health, rust cooling pipes, and to reduce boiler inlet pressure
10/03/2024 to 11/05/2024 (2 months)
Dust generation -1380 tons to 1640 tons/months &
Boiler inlet pressure -1.21kpa to -0.78kpa

## Slide 22
IMPACT OF THE PROBLEM
STEP-3: DEFINE THE PROBLEM
Thermal variations may cause the cooling pipe puncture in the primary duct catcher, leading to welding fractures that affect the chain conveyor's health
Corrosion of cooling pipes
Dust accumulation inside PDC hoppers, which increases boiler inlet pressure.
Adverse effect on chain conveyor's life & high maintenance cost
JSW Steel Ltd, Dolvi

## Slide 23
STEP - 4
ANALYZE THE PROBLEMS
JSW Steel Ltd, Dolvi
Tools & technique used : Check sheet, graph,4W1h analysis

## Slide 24
JSW Steel Ltd, Dolvi
4W-1H ANALYSIS
Step 4 Analyse the problem
WHAT | WHERE | WHEN | WHO | HOW MUCH
Dust Generation | CDQ Primary Dust Catcher | During Continuous Operation of CDQ | CDQ Operation | 1380tons to 1640 tons/month
Boiler Inlet Pressure (P6) | CDQ Primary Dust Catcher | During Continuous Operation of CDQ | CDQ Operation | -1.21kpa to -0.78kpa

## Slide 25
Step 4 Analyse the problem
DATA BASE- BEFORE
Chart: Dust Genenration before
| October | November | December | January
 | 1385 | 1349 | 1295 | 1283

## Slide 26
Step 4 Analyse the problem
DATA BASE- BEFORE
JSW Steel Ltd, Dolvi
Chart: Boiler Inlet pressure before
| October | November | December | January
 | -1.06 | -1.1 | -1.18 | -1.28

## Slide 27
JSW Steel Ltd, Dolvi
STEP - 5 IDENTIFY CAUSES
Tools : Cause and Effect diagram

## Slide 28
LIST OF CAUSES
Step 5 Identify the causes
JSW Steel Ltd, Dolvi
Sr.No | Causes
1 | Hot dust accumulation inside cooling pipes for longer duration
2 | Excess discharge through hoppers
3 | Insufficient flow of cooling water inside jacket
4 | Cooling water quality affects on pipes (like corrosion)
5 | Frequent SDC PDC chain conveyor breakdown
6 | Chamber silos RAV issue like jamming, resulting in chain conveyors stoppage
7 | PDC nitrogen valve jam
8 | Cooling pipes chocking by refractory material
9 | Hammering effect in conical portion
10 | Dust jamming issue
11 | Coke jamming(coke floating) issue (coke stucking inside pipes)

## Slide 29
JSW Steel Ltd, Dolvi
CAUSE & EFFECT DIAGRAM
Step 5 Identify the causes
Cooling water pipe leakage
Man
Machine
Material
Method
Conveyor maintenance
Hot dust accumulation inside cooling pipes for longer duration
Excess discharge through hoppers
Cooling water quality affects on pipes (like corrosion)
Cooling pipes chocking by refractory material
Hammering effect in conical portion
Dust jamming issue
Coke jamming(coke floating) issue
Interlock timing of dust discharge
Frequent SDC PDC chain conveyor breakdown

## Slide 30
JSW Steel Ltd, Dolvi
STEP - 6 IDENTIFY ROOT CAUSES
Tools & technique used : Fish bone and why -why analysis

## Slide 31
JSW Steel Ltd, Dolvi
LIST OF ROOT CAUSES
Step 6 Identify root causes
Sr.NO | PROBABLE ROOT CAUSES
1 | Hot dust accumulation inside cooling pipes for longer duration
2 | Excess discharge through hoppers
3 | Cooling water quality affects on pipes (like corrosion)
4 | Cooling pipes chocking by refractory material
5 | Coke jamming(coke floating) issue (coke stucking inside pipes)

## Slide 32
JSW Steel Ltd, Dolvi
VALIDATATION OF ROOT CAUSES
Step 6 Identify root causes
Sr.No | ROOT CAUSE | OBSERVATION | VALID/INVALID
1 | Hot dust accumulation inside cooling pipes for longer duration | Increase in TT(Temperature transmitter) | VALID
2 | Excess discharge through hoppers | Physical observation | VALID
3 | Cooling water quality affects on pipes (like corrosion) | Cleaning done | VALID
4 | Cooling pipes chocking by refractory material | Physical observation | VALID
5 | Coke jamming(coke floating) issue (coke stucking inside pipes) | Physical observation | VALID
6 | PDC nitrogen valve jam | Physical observation | INVALID

## Slide 33
JSW Steel Ltd, Dolvi
CONFIRMED VALID ROOT CAUSES
Step 6 Identify root causes
Sr.No | VALID ROOT CAUSES
1 | Hot dust accumulation inside cooling pipes for longer duration
2 | Excess discharge through hoppers
3 | Cooling water quality affects on pipes (like corrosion)

## Slide 34
JSW Steel Ltd, Dolvi
Step 7: DATA ANALYSIS

## Slide 35
Step 7: DATA ANALYSIS
BREAK UP OF VALID ROOT CAUSES
Chart: 
| October | November | December | January
Discharge time(manually) in sec | 240 | 226 | 215 | 189
Dust Temp (TT) | 149 | 136 | 115 | 82
Before Implementation Data

## Slide 36
Step 7: DATA ANALYSIS
Before Implementation Data
Chart: Dust generation Before
Before | 1380
Chart: Boiler inlet pressure Before
Before | -1.21

## Slide 37
JSW Steel Ltd, Dolvi
STEP 8: DEVELOPING SOLUTIONS
Through Brain Storming

## Slide 38
PROPOSED SOLUTION
Description of solution to cause:
We discovered this issue when water leakage from the PDC cooling pipe began to leak, causing damage to the chain conveyor linkage and affecting the life span of the chain conveyor, so during shutdown time, we opened the conical portion of the PDC 2 hopper and checked and which need to be arrest leakage tubes.
Identified but it should be arrest punctured cooling pipe asap

## Slide 39
PROPOSED SOLUTION
Description of solution to cause: Hot dust accumulation inside cooling pipes for longer duration & Excess discharge through hoppers
To prevent hot dust accumulation inside cooling pipes for longer durations and excess discharge through hoppers, we can change discharge technique from manual to efficient technique of adding a timer to discharge so that dust will come in proper time and will not increase the temperature of dust.
Dust discharging trend (manually)Before

## Slide 40
JSW Steel Ltd, Dolvi
STEP 9: FORSEEING PROBABLE RESISTANCES

## Slide 41
JSW Steel Ltd, Dolvi
STEP 9: FORSEEING PROBABLE RESISTANCES
Sr no | Queries | Raised by | Answer given by QC members
1 | How much time is required to arrest puncture will it be increase dust generation and boiler inlet pressure | Mr. Varaprasad (Operation) | Will isolate the line and check the abnormalities and arresting will be completed by 5-6 hrs and surely it will increases dust generation and other parameters
2 | How far is it feasible ? | Mr.Gopinath (Mechanical) | It is 100 % feasible because the parameters will be in control as monitored for whole day
3 | What about Safety? | Mr. Darshan Dave (Safety) | All Solution are safe and easy to Operate
4 | What about the cost? | Arun Kumar (Electrical) | No additional cost done with available materials

## Slide 42
JSW Steel Ltd, Dolvi
STEP 10: TRIAL IMPLIMENTATION

## Slide 43
Problem is selected and Impacts of the problem are quantified
Two root causes are identified & validated based on experience & observation
And for which solutions are developed.
Proposed solutions are implemented & results are checked
SOP has been modified accordingly
Outcome of which is found to be very effective.
DEMING CYCLE

## Slide 44
Description of solution to cause:
We discovered this issue when water leakage from the PDC cooling pipe began to leak, causing damage to the chain conveyor linkage and affecting the life span of the chain conveyor, so during shutdown time, we opened the conical portion of the PDC 2 hopper and checked and arrested the leakage tubes.
Identified and arrested punctured cooling pipe

## Slide 45
Description of solution to cause: Hot dust accumulation inside cooling pipes for longer duration & Excess discharge through hoppers
To prevent hot dust accumulation inside cooling pipes for longer durations and excess discharge through hoppers, we can change discharge technique from manual to efficient technique of adding a timer to discharge so that dust will come in proper time and will not increase the temperature of dust.
Dust discharging trend (manually)Before
Timer implementation
Uniform Discharge accordingly timer

## Slide 46
JSW Steel Ltd, Dolvi
BEFORE – AFTER COMPARISON
Chart: 
| October | November | December | January | february
 | 1385 | 1349 | 1295 | 1283 | 1640
Chart: 
| October | November | December | January | february
 | -1.06 | -1.1 | -1.18 | -1.28 | -0.78
Boiler inlet pressure data from OCT 2023 –Feb 2024
Dust generation data from OCT 2023 –Feb 2024

## Slide 47
JSW Steel Ltd, Dolvi
Chart: Dust Generation (monthly)
| Before | After
 | 1380 | 1640
Chart: Boiler Inlet Pressure (P6)
| Before | After
 | -1.21 | -0.78
BEFORE – AFTER COMPARISON

## Slide 48
JSW Steel Ltd, Dolvi
STEP 11: REGULER IMPLEMENTATION

## Slide 49
JSW Steel Ltd, Dolvi
GANTT CHART
Chart: 
| 45383 | 45389 | 45395 | 45401 | 45414 | 45383 | 45383
 | 8 | 7 | 6 | 5 | 4 | 0 | 0
 | 0 | 0
 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 50
JSW Steel Ltd, Dolvi
TANGIBLE AND INTAGIBLE BENEFITS
Tangible Benefits | Intangible Benefits
1) Dust generation cost (monthly)=260 Tons * Dust cost per ton | 1) Equipment Healthiness
2) Dust discharge time gets reduced to half the before, so equipment healthiness is beneficial | 2) Easy manpower handling
3)5 Housekeeping manpower cost for manually dust removal | 3) Less anxiety when it comes to periodically manually discharge

## Slide 51
JSW Steel Ltd, Dolvi
FOLLOW-UP/REVIEW AND
RECURRENCE PREVENTION
SMP reviewed again to have a better results
SOP provided incase of external discharge
Training given to operators for the procedure
Checklist provided in control room for monitoring discharge

## Slide 52
JSW Steel Ltd, Dolvi
FOLLOW-UP/REVIEW AND
RECURRENCE PREVENTION

## Slide 53
JSW Steel Ltd, Dolvi
FOLLOW-UP/REVIEW AND
RECURRENCE PREVENTION

## Slide 54
JSW Steel Ltd, Dolvi
FOLLOW-UP/REVIEW AND
RECURRENCE PREVENTION

## Slide 55
JSW Steel Ltd, Dolvi
FOLLOW-UP/REVIEW AND
RECURRENCE PREVENTION

## Slide 56
JSW Steel Ltd, Dolvi
PROJECT COMPLETION SHEET

## Slide 57
JSW Steel Ltd, Dolvi